Geomoprhometric References And Notes 0.1.1

Topography is one of the most important controls within the dynamics of drainage basins. Geomorphometry deals with surface altitude, gradient, distance and area, and express quantitatively the measurement of landforms (EVANS, 1972).

Useful geomorphometrics:

Surface area of catchment

Surface area to planar area ratio

Volume to potential volume ratio

Histogram of heights – elevation vs area - hypsometric curve

Mean slope

Standard deviation of slope

P = Perimeter; 
L = Basin length; 
A = Area; 
Vp = Basin potential volume; 
Va = Basin actual volume; 
Rf = Form factor = A/L2; 
Kc = Compactness coefficient = 0.282 P / A0.5; 
Re = Elongation ratio = 1.128 (A0.5/L); 
W = Width of watershed = A/L; 
Rc = Circularity ratio 4 A/P2; 
Lr = Length ratio = L (PA)/ L (SM); 
Pr = Perimeter ratio = P (PA)/ P (SM); 
Ar = Length ratio = A (PA)/ A (SM); 
Hi = Hypsometric integral = Va / Vp; 
Hr = Hypsometric ratio = (Vp - Va )/ Va;

Aguilar J.A.P, Perez J.M.R., GIS (Idrisi) Analysis of Digital Elevation Models for the Extraction of Drainage Basin Geomorphometric Properties. http://sigte.udg.es/idrisi/recursos/secundari/reunion1/htmls/14/index.htm

DONKER, N. H. W., 1992: Automatic extraction of catchment hydrologic properties from digital elevation data. ITC Journal 3, 257-265.

GARDNER, T. W., CONNORS SASOWSHY, K. and DAY, R. L., 1990: Automated extraction of geomorphometric properties from digital elevation data. Z. Geomorph. N. F. 80, 57-68.

GARG, P.K. and HARRISON, A. R., 1990: Quantitative representation of land-surface morphology from digital elevation models. In: Proceedings of the 4th international symposium on spatial data handling. Vol. 1, Zurich, 273-282.

Evans I.S. (1972) General Geomorphometry, derivatives of altitude, and descriptive statistics. In Chorley R.J. (ed.) Spatial Analysis in Geomorphology. Mathuen & co ltd 17-92.

Frauenfelder R., Schneider B. (2002) Geomorphometric modelling of rock Glaciers, an extended abstract

Kokkas N.A., Miliaresis G.Ch. (2004) Geomorphometric mapping of Grand Canyon from the 1-degree USGS DEMs

Korup O. (2003) Geomorphometric Characteristics of New Zealand landslide dams. Engineering Geology 73.1 May 2004 pp13-35

Korup O. (2004) Geomorphic Hazard Assessmen of landslide dams in South Westland New Zealand: Fundamental Problems and approaches. Geomorphology 66.2 March 2005 pp167-188

Horsch B. (2003) Modelling the spatial distribution of montane and subalpine forests in the central alps using digital elevation models. Ecological modelling 168.3 October 2003 pp267-282.

Mark D. (1975) Geomorphometric parameters, a review and evaluation. Geographiska Annaler 57A 1461-1467.

Pike R. (1995) Geomorphometry-process, practice and prospects. Zeitschrift. Geomorphologie N.F. Suppl. Bd 101:221-238

## Pike R.J. (1998) Web Resources Compiled For Terrain Modeling

http://www.agu.org/eos_elec/97260e.html

Pike R.J. (2002) A Bibliography of Terrain Modelling (Geomorphometry), the Quantitative Representation of Topography – Supplement 4.0 USGS Open File Report 02-465  geopubs.wr.usgs.gov/open-file/of02-465/of02-465.pdf

STRAHLER, A. N.,  1954: Quantitative geomorphology of erosional landscapes. 19th Intern. Geol. Cong., Algiers, 341-354.

Fortey R (2004) The Earth: An Intimate History. Knopf/Random House
ISBN: 0375406263